## Slide 1
Python-Based Preprocessing for NOS-OFS
Replacing Legacy Shell+Fortran with nos-utils Mansur Jisan | NOAA NOS/CO-OPS | 2026

## Slide 2
The Problem: Legacy Preprocessing Pipeline
• ~3,700 lines of shell scripts calling Fortran executables
• 20+ module loads required (Intel, MPI, HDF5, NetCDF, BUFR, G2...)
• Each OFS requires copying and modifying 4+ scripts
• No unit tests — bugs caught only in production
• Debugging: read 56,000-line PBS error logs
• Adding new data sources (RRFS, GEFS) = major shell surgery
Current shell chain:
  - exnos_ofs_prep.sh → nos_ofs_create_forcing_met.sh (1,507 lines)
  - → nos_ofs_create_forcing_obc.sh (1,113 lines)
  - → nos_ofs_create_forcing_river.sh (299 lines)
  - → nos_ofs_prep_schism_ctl.sh (253 lines)

## Slide 3
The Solution: nos-utils Python Package
• Standalone Python package — no dependency on existing codebase
• Each processor independently testable
• YAML configuration with inheritance
• Works for any SCHISM-based OFS (SECOFS, STOFS-3D-ATL, CREOFS)
• Dual GRIB2 backends: wgrib2 (prod) + cfgrib (dev)
• 124 unit tests, runs in 2.4 seconds
from nos_utils.config import ForcingConfig from nos_utils.forcing import GFSProcessor config = ForcingConfig.for_secofs( pdy="20260403", cyc=0 ) gfs = GFSProcessor( config, "/data/gfs", "/data/sflux", phase="nowcast" ) result = gfs.process() # → sflux_air_1.1.nc # sflux_rad_1.1.nc # sflux_prc_1.1.nc

## Slide 4
Package Architecture
Atmospheric Forcing:
  - GFSProcessor — 0.25° global, hourly, 18 variables
  - HRRRProcessor — 3km CONUS, Lambert Conformal → lat/lon regrid
  - GEFSProcessor — Ensemble, 3-hourly, RH→SPFH conversion
•
Ocean Boundary:
  - RTOFSProcessor — Interpolate to SCHISM boundary nodes from hgrid.ll
  - SchismGrid reader — parses any SCHISM grid (1.68M nodes, 321 MB)
•
River / Tidal / Model Config:
  - NWMProcessor — NWM channel_rt with climatology fallback
  - TidalProcessor — bctides.in with phase-aware nodal corrections
  - ParamNmlProcessor — param.nml with ihot=1 (nowcast) / ihot=2 (forecast)
•
Shared Writers:
  - SfluxWriter — day-split NetCDF, monotonic time validation
  - DATMWriter — UFS-Coastal DATM format

## Slide 5
Configuration: .ctl → YAML with Inheritance
• **Before:** Flat .ctl file, ~100 shell variables per OFS
• **After:** YAML with _base inheritance, ~40 lines per OFS
• Adding a new OFS: 10-line YAML instead of copying 4 scripts
• ForcingConfig.from_yaml() reads grid, forcing, model sections
• Factory methods: for_secofs(), for_stofs_3d_atl(), for_ensemble()
# secofs.yaml _base: schism # Inherits 100+ defaults grid: domain: lon_min: -88 lon_max: -63 lat_min: 17 lat_max: 40 files: horizontal_ll: secofs.hgrid.ll forcing: atmospheric: primary: GFS secondary: HRRR met_num: 2 ocean: nudging: enabled: true timescale_seconds: 10800 model: run: nowcast_hours: 6 forecast_hours: 48

## Slide 6
Ocean Boundary: Pure Python Replacement
• **Legacy:** Fortran gen_3Dth_from_hycom (~2000 lines compiled)
•
Python replacement (3 steps):
  - 1. Parse hgrid.ll → extract 1,494 boundary nodes (4 segments)
  - 2. Build nearest-neighbor index (cached per RTOFS grid shape)
  - 3. Interpolate RTOFS T/S/SSH/UV to boundary nodes × depth levels
•
Output (matches Fortran format):
  - elev2D.th.nc: (138, 1494) — SSH at boundary
  - TEM_3D.th.nc: (72, 1494, 40) — Temperature
  - SAL_3D.th.nc: (72, 1494, 40) — Salinity
  - uv3D.th.nc: (72, 1494, 40, 2) — Velocity
•
• Works with any SCHISM OFS — just change the grid file

## Slide 7
Phase-Aware Processing: Nowcast vs Forecast
• Each processor receives phase parameter — determines time window
•
Nowcast:
  - Start: time_hotstart (from restart file, e.g., 04-02 12:00)
  - End: cycle time (04-03 00:00)
  - param.nml: rnday=0.5, ihot=1, start=hotstart_time
  - GFS: kept 16/61 files within window
•
Forecast:
  - Start: cycle time (04-03 00:00)
  - End: cycle + 48h (04-05 00:00)
  - param.nml: rnday=2.0, ihot=2, start=cycle_time
  - GFS: kept 52/61 files within window
•
• Legacy uses separate code paths; Python uses single phase parameter

## Slide 8
Integration with NCO Operational Workflow
• Zero changes to existing workflow — feature flag activation
•
• **Hybrid mode** (USE_PYTHON_PREP=YES):
  - Python: met forcing, param.nml, bctides.in
  - Fortran: OBC boundary interpolation, river forcing
•
• **Full Python mode** (+ FULL_PYTHON_PREP=YES):
  - Python handles everything including OBC/river
  - No Fortran executables needed
•
• nco_bridge.py translates NCO env vars → ForcingConfig:
  - PDY, cyc, COMINgfs, FIXofs → config + paths dict
  - Resolves relative file paths against FIXofs
  - Archive outputs with NCO naming convention
# PBS script — one line change export USE_PYTHON_PREP=YES export FULL_PYTHON_PREP=YES ${HOMEnos}/jobs/JNOS_OFS_PREP # Or use CLI directly nos-utils prep \ --ofs secofs \ --pdy 20260403 --cyc 0 \ --gfs /data/gfs \ --hrrr /data/hrrr \ --fix /data/fix/secofs \ --output /work/prep

## Slide 9
Resource Comparison: Legacy vs Python
 | Legacy (Shell+Fortran) | Python (nos-utils)
CPUs required | 128 (MPI) | 1
HPC modules | 20+ (Intel, MPI, HDF5, BUFR...) | 5 (Python, wgrib2, nco)
Compile step | Required (Fortran) | None
Lines of code | ~3,700 shell + Fortran | ~7,500 Python
Unit tests | 0 | 124
Config format | .ctl (flat) | YAML (inherited)
Add new OFS | Copy+modify 4 scripts | 10-line YAML file
Debugging | 56K-line PBS logs | Structured Python logging

## Slide 10
WCOSS2 Validation: Python vs Legacy Output
Byte-for-byte identical (hybrid mode):
  - OBC tar: 729 MB ✓
  - River tar: 470 KB ✓
  - init.nowcast.nc: 18 GB ✓
  - Time markers: all 4 files ✓
•
Functionally equivalent:
  - param.nml: rnday, ihot, start_time all match
  - bctides.in: 23,909 lines, phase-aware start + nodal corrections
  - GFS sflux: same wind/pressure/temperature patterns at stations
  - HRRR sflux: regridded 834×768, 58% CONUS coverage
•
Full Python OBC (new):
  - elev2D.th.nc: (138, 1494) boundary nodes — correct dimensions
  - TEM/SAL_3D: (72, 1494, 40) — matching Fortran shape

## Slide 11
Roadmap
Phase 2: SCHISM model validation
  - Run SCHISM with Python-generated forcing
  - Compare station water levels: target RMSE < 1 cm
  - Multi-cycle consistency (3 consecutive cycles)
•
Phase 3: STOFS-3D-ATL
  - Larger domain, 24h nowcast, 108h forecast
  - 7,690 river reaches, 51 vertical levels
  - Same nos-utils package — just different YAML config
•
Phase 4: Operational deployment
  - 30-day parallel run (Python + legacy side-by-side)
  - CI/CD pipeline with GitHub Actions
  - Retire legacy shell scripts
•
Phase 5: UFS-Coastal
  - DATM forcing (datm_forcing.nc + ESMF mesh)
  - Blended GFS+HRRR for CDEPS coupling

## Slide 12
nos-utils
github.com/mansurjisan/nos-utils github.com/mansurjisan/nos-workflow 124 unit tests | 20 modules | Production-validated on WCOSS2